## Slide 1: PacketCloud: an Open Platform for Elastic In-network Services
Yang Chen1, Bingyang Liu2, Yu Chen1, Ang Li1,
Xiaowei Yang1, Jun Bi2
1Duke University 2Tsinghua University
ychen@cs.duke.edu

## Slide 2: The End-to-End Principle of the Internet
Routers: best-effort forwarding
End systems: all end-to-end functions…
TCP
TCP
A simple design for IP routers:
low complexity, high robustness
S
D
Designed 30+ years ago
Background – Design – Evaluation – Contributions

## Slide 3: The Ossification of the Internet
In-network Services are highly desired
Background – Design – Evaluation – Contributions
Popular contents are transferred again and again
Can we avoid the redundant transmission?
Numerous malicious attacks
Can we block the malicious traffic before they have arrived the destination?
Widely used mobile devices with limited battery energy
Can we offload the computational tasks for mobile devices?

## Slide 4: In-network Services: Today’s Practice
ISPs have deployed numerous standalone, specialized middleboxes at strategic network locations
Third-party (content/application) providers need to collaborate with ISPs
Enhancing the user experience
Optimizing the network traffic
Fixed capacity for each middlebox (over provisioning)
The available resources of different middleboxes cannot be shared
Background – Design – Evaluation – Contributions

## Slide 5: Our Goal: a Better In-network Service Hosting Platform
Efficient
Elastic
Open
Rewards for ISPs
Background – Design – Evaluation – Contributions
Design requirements

## Slide 6: Related Work
CoMb: consolidation of middleboxes [Sekar et al., NSDI’12]
  Supporting only trusted/reliable services
  Not open to third-party providers
  Vulnerable to unexpected service crash and malicious attacks
APLOMB: outsourcing to public clouds [Sherry et al., SIGCOMM’12]
  Unwanted interdomain traffic
  Data ownership problems
Background – Design – Evaluation – Contributions

## Slide 7: Underlying Network Architecture
  Conventional IP or clean-slate architectures?
  Technical trend: rapid development of mobile platforms and applications
We focus on MobilityFirst (MF)
A mobile-centric architecture for the future Internet, one of the four NSF Future Internet Architecture (FIA) projects
Background – Design – Evaluation – Contributions

## Slide 8: MF: Prominent Features
A fixed globally unique identifier (GUID) for every network entity
  Robust to host mobility (keeping the end-to-end connection)
Optimized reliable data delivery
  Robust to data links with varying qualities (e.g., wireless links)
ISP X
ISP Y
ISP Z
GUID=10
3X Throughput of TCP
GUID=20
Background – Design – Evaluation – Contributions

## Slide 9: PacketCloud: Overview
Cloudlet
Cloudlet
New York
Washington
Cloudlets to support elastic in-network services
Background – Design – Evaluation – Contributions

## Slide 10: Inside a Cloudlet
 | CPU (cores) | Mem (GB) | Disk (GB) | BW (Gbps)
N1 | 7/1 | 1/1 | 250/50 | 5/5
N2 | 4/4 | 0/2 | 50/200 | 9/1
… | … | … | … | …
Reserved / Available
Resource Table (time slot: [t0, t1])
……
Serv 2
Serv 1
Cloudlet
Controller
DEMUX Rules
Background – Design – Evaluation – Contributions

## Slide 11: Virtualizing Computation Nodes
One computation node: multiple virtual instances (VIs)
Each service will be hosted by a dedicated VI
  Assigned with a globally routable GUID
  Programmable: supporting Linux-based general purpose services (extensible)
  Elastic resource allocation
VI
VI
VI
Linux Containers (lxc)
Background – Design – Evaluation – Contributions
3 cores
1 core

## Slide 12: ISP-wide Resource Management
Cloudlet in NY
Cloudlet in LA
Cloudlet in DC
A logically centralized domain controller
Every cloudlet controller is one of its agents
Keeps an aggregate view of the resources of all cloudlets
Provides a web-based reservation interface for service providers
Background – Design – Evaluation – Contributions

## Slide 13: Virtual Instance Reservation
Time slot
VI type
Location (optional)
Oct 20, 2013
9AM-10AM
Small Instance:
2 cores, 1 GB Mem.
10GB Disk, 1Gbps BW
Least-loaded cloudlet
Service identifier (SID):
Globally unique and routable
Upload the program
Background – Design – Evaluation – Contributions

## Slide 14: User Requested Services
S
D
Payload
SID=30
SID=30
Data delivery rule:
Source  Selected service  Destination
s
D
  Use Cases:
  Transcoder
  Protocol translator
  Context aware services
  Anonymous communications
Activated by
end users
Background – Design – Evaluation – Contributions

## Slide 15: Transparent Services
S
D
Payload
Service X
Intercept!!!
DEMUX Rule:
a specified source/destination GUID
a specified field in the chunk header
……
Activated by ISPs
Serving the legacy end-to-end traffic
Use Cases
Content caches
Wide Area Network (WAN) optimizers
On-path encryption/decryption systems
Intrucsion detection systems
Background – Design – Evaluation – Contributions
S
D

## Slide 16: Reliability and Security
Background – Design – Evaluation – Contributions
Service Failure
Inside the VI
Malicious Service
All in/out traffic can be inspected
Malicious DEMUX rule
Proof of GUID ownership required
Excessive resource usage
Reserving dedicated resources Tiered pricing

## Slide 17: A Proof-of-concept Prototype
Service-aware MF software router
  Based on the latest MF prototype (using Click Modular Router)
  Guiding the MF routers to identify and discover PacketCloud services
Implemented services
  Protocol translator (user requested)
  WAN optimizer (transparent)
  Intrusion detection system (transparent)
  Secure communication module (transparent)
  (more are coming…)
Background – Design – Evaluation – Contributions

## Slide 18: Test and Evaluation
Tested in both wired/wireless environments
Evaluation results
  Scalability
  Delay Penalty
Background – Design – Evaluation – Contributions

## Slide 19: Scalability
How much traffic a cloudlet can handle?
  Starting from a single computation node…
  Hardware: bpc2133 nodes on Deterlab (Quad Core processor running at 2.13GHz, 1Gbps NIC)
  Service complexity: AES encryption (computationally intensive)
  One node can handle traffic as fast as 500~600Mbps
20 nodes in a Cloudlet  10+Gbps
A modest estimation
Background – Design – Evaluation – Contributions

## Slide 20: Delay Penalty
100Mbps,30ms,0.1% Loss
A
R
B
Traffic Encryptor
100Mbps,30ms,0.1% Loss
Background – Design – Evaluation – Contributions
When chunk size = 1MB, the average per-chunk delay penalty is still < 30ms (smaller than the additional delay of sending an individual IP packet using 3G)
Want a smaller delay penalty?
Better CPU
10Gbps NIC
Smaller protocol data unit

## Slide 21: Contributions
A “cloud-like” platform to host in-network services
  Elastic services: scaling up/down according to traffic demand
  Efficient resource sharing
  Open to third-party providers
  Viable economic rewards for ISPs
A number of viable use cases
A proof-of-concept prototype and evaluation
Background – Design – Evaluation – Contributions

## Slide 22: Future Works
Cloudlet deployment strategy
  Network topology, user behavior, and resource availability
Economic Models
  Financial links among diﬀerent Internet entities, i.e., users, ISPs, and third-party providers
Background – Design – Evaluation – Contributions

## Slide 23: Acknowledgements
Feixong Zhang, Kiran Nagaraja, and Dipankar Raychaudhuri (Rutgers University)
Qiang Cao, Xin Wu, Theophilus A. Benson (Duke University)